## Slide 1: Working Principle
The working principle of the linear launcher depends upon the law of conservation of energy in which first energy is stored in the form of elastic potential energy inside the spring and then this energy is released to attain certain kinetic energy.

## Slide 2: Structure Analysis

## Slide 3
Base plate
Moveable Plate
Pipe
Striking Rod
Trigger
Link
1
6
2
5
4
3

## Slide 4
The Base Plate
And
The Moveable plate
The base plate is made of the plastic on which moveable plate is connected. The base plate is bearing all weight and is supporting moveable plate over it.
The moveable plate is also made of the plastic and is supporting the pipe in which the ball is placed. It can move with the help of link which is connected with the base plate and moveable plate.

## Slide 5: The Pipe And The striking rod
Both of the materials are made of the plastic. The rod is put inside the pipe along the spring on it. When the rod is pulled back the spring get compressed and the energy is stored inside it. The rod is locked at its pulled position by locking it to the trigger.

## Slide 6: The trigger and the link
The trigger is made of the plastic. It is connected with the moveable plate and its one end is present at the empty slot present in the center of the moveable plate which serves as the lock. While the other end is act as trigger.
The link is also made of the plastic. It is the connection between the base plate and the moveable plate. It serves as the angle changer between the two plates due to which the angle of projection also changes.

## Slide 7: Working principle
When the striking rod is pulled back the spring over it got compressed and then it stores the elastic potential energy in it. The rod can be locked with the trigger. So when the small external force is applied on the trigger the rod got unlocked and it launches the ball by changing the potential energy into the kinetic energy and the ball hits the certain target according to the calculation. We can change the angle of projection with the help of the link present between the plates.